## Slide 1
East Avenues Safety Study
D5 Community Cabinet
Molly Lanphier, Community Designer

## Slide 2: Study Boundaries
E 13th Avenue
E 14th Avenue
E 16th Avenue
East 17th Avenue
East 18th Avenue
Broadway  Yosemite St
Detroit Colorado Blvd
Colorado Blvd  Yosemite St
Studied through a transit Speed & Reliability Study

## Slide 3: Crash History 2018-2022
Chart: 
| East 13th Ave | East 14th Ave | East 17th Ave
Property Damage Only Crashes | 711 | 824 | 272
Bodily Injury Crashes | 195 | 250 | 79
Ped/ Bike Crashes | 35 | 44 | 6
Fatal Crashes | 3 | 2 | 1
1120
358

## Slide 4: Percent of Vehicles Speeding by Street
Chart: 
| East 13th Ave | East 14th Ave | East 17th Ave
% Speeding (Over Speed Limit) | 57 | 61 | 76
% Excessively Speeding (>10 MPH Over Speed Limit) | 6 | 9 | 9

## Slide 5: Themes from Outreach
Chart: 
| Drivers not Yielding to Pedestrians | Red Light Running | Difficulty Crossing to Visibility Issues | Inadequate or missing pedestrian infrastructure | Speeding
Number of Responses | 105 | 113 | 160 | 161 | 400

## Slide 6: Speeding Proposed Solutions
Speed Cushions
Bulbouts
Chicanes
Signal Coordination

## Slide 7: Speeding Additional Solutions
Two-Way
Conversion
Lane Reduction
Protected
Bike Lanes

## Slide 8: Broadside Crashes Proposed Solutions at Unsignalized Intersections
Increase Sight Distance
Daylighting- Increasing sight distance by prohibiting parking by an additional 20 feet

## Slide 9: Near Term Implementation
Bulbouts
    13th Ave & Ogden, Corona, Downing and Marion
    14th Ave & Washington, Corona, Marion and Lafayette
Two-Way Conversion
    13th & 14th from Quebec to Yosemite- Spring/ Summer 2025

## Slide 10: Next Steps
Study the feasibility of the longer-term solutions post BRT construction
Identify Additional Funding
Keep Collecting Data via 311 and DPD

## Slide 11: Questions? Website: DenverGov.org/EastAveSafety Email: EastAveSafety@DenverGov.org
Notes: 311